## Slide 1: VHDL_03: Hierarchical VHDL and Simulation
Structure of a Hierarchical Design
  Component Declaration and Instantiations
Testbench
  Device-Under-Test, Stimuli, Clock-Generator, Checks
Simulation
  Tools, Libraries und Script
Mini-Exercise
  Analysis of Code and Testbench for simple_dff_circ.vhd (analyse code and draw RTL + timing diagrams)

## Slide 2: Hierarchical VHDL Design

## Slide 3: Hierarchical Design
3

## Slide 4: Matroschka Doll

## Slide 5: Hierarchical VHDL Design or Structural Modeling
Top_Level
Peripherals
Prozessor
UART
uC Core
RAM
ROM
Audio Block
Video Block
Parallel Port
Top_Level
Peripherals
Prozessor
UART
uC Core
RAM
ROM
Audio Block
Video Block

## Slide 6: Example of a hierarchical Design
Objective: replace this top level schematics by a VHDL description.
hex2sevseg.vhd
countdown.vhd

## Slide 7: STEP-1: The top-level has an Entity
countdown.vhd
hex2sevseg.vhd
ENTITY top_level IS
PORT(
clock : IN std_logic;
rst_n : IN std_logic;
start : IN std_logic;
segmente : OUT std_logic_vector(6 downto 0)
);
END top_level ;

## Slide 8: STEP-2: The Top Level has an Architecture with Component Declarations
ARCHITECTURE struct OF top_level IS
-- components and signals declaration
COMPONENT hex2sevseg
PORT( hexa_i : IN std_logic_vector(3 downto 0);
seg_o : OUT std_logic_vector(6 downto 0)
);
END COMPONENT;
COMPONENT countdown
PORT( clk,
reset_n : IN std_logic;
start_i : IN std_logic;
count_o : OUT std_logic_vector(3 downto 0)
);
END COMPONENT;
SIGNAL count2hexa : std_logic_vector(3 downto 0);
BEGIN
Connection signal:
count2hexa

## Slide 9: STEP-3: The components are instantiated on the top level architecture description
BEGIN
inst_countdown_1: countdown
PORT MAP (
clk => clock,
reset_n => rst_n,
start_i => start,
count_o => count2hexa
);
inst_hex2sevenseg_1: hex2sevseg
PORT MAP (
hexa_i => count2hexa,
seg_o => segmente
);
END struct;
Signal Names in the top architecture
containing the instance
Ports of the Component Entity (see Component Declaration)
Instance Name (freely selectable)
count2hexa
Entity Name
Instance = unique realisation of component

## Slide 10: Overview: Example of a Top Level Architecture
ARCHITECTURE struct OF top_level IS
COMPONENT hex2sevseg PORT(
hexa_i : IN std_logic_vector(3 downto 0);
seg_o : OUT std_logic_vector(6 downto 0));
END COMPONENT;
COMPONENT countdown
PORT( clk,reset_n : IN std_logic;
start_i : IN std_logic;
count_o : OUT std_logic_vector(3 downto 0));
END COMPONENT;
SIGNAL count2hexa : std_logic_vector(3 downto 0);
BEGIN
inst_countdown_1: countdown
PORT MAP (clk => clock,
reset_n => rst_n,
start_i => start,
count_o => count2hexa
);
inst_hex2sevenseg_1: hex2sevseg
PORT MAP (hexa_i => count2hexa,
seg_o => segmente
);
END struct;

## Slide 11: Exercise-1: Draw the schematics described below
LIBRARY IEEE;
USE IEEE.std_logic_1164.ALL;
ENTITY dekoder_einfach IS PORT (
A: IN std_logic;
B: IN std_logic;
C: IN std_logic;
D: IN std_logic;
Z: OUT std_logic );
END dekoder_einfach ;
ARCHITECTURE structural OF dekoder_einfach IS
SIGNAL int1: std_logic;
COMPONENT nand2
PORT ( in1,in2 : IN std_logic;
outp : OUT std_logic );
END COMPONENT;
COMPONENT and3
PORT ( in1,in2,in3 : IN std_logic;
outp : OUT std_logic );
END COMPONENT;
BEGIN
inst1: nand2 PORT MAP (
in1 => A,
in2 => B,
outp => int1 );
inst2: and3 PORT MAP (
in1 => int1,
in2 => C,
in3 => D,
outp => Z );
END ARCHITECTURE structural;

## Slide 12: VHDL Simulation

## Slide 13: Simulation Tool = Modelsim
Stimuli Generator
Clock
Generator
Entity «Testbench»
DUT (device under test)
Checks
Stimuli & Check Process

## Slide 14: Testbench is a hierarchy level above Top Level
top_level
top_level_testbench
Stimuli:
Simulationsausgabe:
ENTITY testbench_counter IS
END testbench_counter;
Visual
Check

## Slide 15: Definition of Component to be tested and connection signals
ARCHITECTURE struct OF testbench_counter IS
COMPONENT top_level
PORT( clock : IN std_logic;
rst_n : IN std_logic;
start : IN std_logic;
segmente : OUT std_logic_vector(6 downto 0));
END COMPONENT;
SIGNAL tb_clock : std_logic;
SIGNAL tb_rst_n : std_logic;
SIGNAL tb_start : std_logic;
SIGNAL tb_segmente : std_logic_vector(6 downto 0);
CONSTANT clk_halfp : time := 20 ns;
BEGIN
tb_clock
tb_rst_n
tb_start
tb_segmente
top_level_testbench

## Slide 16: Instantiation of top_level as Device Under Test (DUT)
BEGIN
DUT: top_level
PORT MAP ( clock => tb_clock,
rst_n => tb_rst_n,
start => tb_start,
segmente => tb_segmente
);
tb_clock
tb_rst_n
tb_start
tb_segmente
top_level_testbench

## Slide 17: Clock Generation for Simulation
…
SIGNAL clk_halfp : time := 20ns;
…
clkgen : PROCESS
BEGIN
clk <= '0';
WAIT FOR 1*clk_halfp;
clk <= '1';
WAIT FOR 1*clk_halfp;
END PROCESS clkgen;
…
END struct;
(Ohne Sensitivity Liste)

## Slide 18: Stimuli Process: simple example
stimuli: PROCESS
BEGIN
tb_rst_n <= '0';
tb_start <= '0';
WAIT FOR 12 * clk_halfp;
tb_rst_n <= '1';
WAIT FOR 2 * clk_halfp;
tb_start <= '1';
WAIT FOR 2 * clk_halfp;
tb_start <= '0';
WAIT FOR 20 * clk_halfp;
tb_start <= '1';
WAIT FOR 2 * clk_halfp;
tb_start <= '0';
WAIT;
END PROCESS stimuli;
END struct;

## Slide 19: Wait Statements
WAIT UNTIL condition;
wait on signal_list;
WAIT FOR time;
wait;
Wait until CLK= ‘1‘;
Wait for 10 nS;
Wait on A,B;
Wait until certain condition is fulfilled
Wait until change of specified signal(s)
Wait for given time period
Undefined wait
Beispiele:

## Slide 20: WAIT Statements
WAIT Statements are sequential and can only appear within processes
By execution of WAIT Statements the process is stopped and all related signal assignments are updated
After the execution of the WAIT statement, the process is resumed (from the same point where stopped)
WAIT is not synthesisable

## Slide 21: Assert Statement
ASSERT condition REPORT string SEVERITY SEVERITY_level ;
Possible levels are: note warning ERROR failure (stops simulation)
Beispiele:
„ASSERT“ allows to build a test during the simulation, generating a report, and select gravity in case of mismatch with expected result.
Assert is ignored by the Synthesis.
ASSERT (A = B) REPORT “A ungleich B“ SEVERITY ERROR ;
ASSERT false REPORT “Test programm beendet“ SEVERITY note ;
Case „Condition“ not fulfilled, a report is generated

## Slide 22
STIMULUS: process
begin
bcd <= "000" ;
WAIT FOR 10 ns;
ASSERT (gray = "000") REPORT "expected "000" " SEVERITY ERROR;
WAIT FOR 100 ns;
bcd <= "111";
WAIT FOR 10 ns;
ASSERT (gray = "100") REPORT "expected „100“ " SEVERITY ERROR;
WAIT FOR 100 ns;
ASSERT false REPORT " --- ALL TESTS PASS ---" SEVERITY FAILURE;
end process;
Example: Testbench for bcd-gray Decoder
«errors» are counted but
do not stop the simulation.
Failure stops the simulation (break up execution)
stops the simulation

## Slide 23: Testbench for Lab3 – Exercise 1.1)
Ausgangssignal wird verglichen

## Slide 24: Einfach_Schaltung
-- Library & Use Statements
LIBRARY ieee;
USE ieee.std_logic_1164.all;
-- Entity Declaration
ENTITY einfach_schaltung IS
PORT (
clock : in std_logic;
reset_n : in std_logic;
data_i : in std_logic;
hold_i : in std_logic;
buff_o : out std_logic
);
END einfach_schaltung;
-- Architecture Declaration
ARCHITECTURE rtl OF einfach_schaltung IS
-- Signals & Constants Declaration
SIGNAL buff, next_buff : std_logic ;
BEGIN
-------------------------------------------
-- Process for combinatorial logic
-------------------------------------------
comb_logic: PROCESS(ALL)
BEGIN
-- hold or update
IF hold_i='1' THEN
next_buff <= buff;
ELSE
next_buff <= data_i;
END IF;
END PROCESS comb_logic;
-------------------------------------------
-- Process for registers (flip-flops)
-------------------------------------------
flip_flops : PROCESS(clock, reset_n)
BEGIN
IF reset_n = '0' THEN
buff <= '0';
ELSIF RISING_EDGE(clock) THEN
buff <= next_buff ;
END IF;
END PROCESS flip_flops;
-------------------------------------------
-- Concurrent Assignements
-- e.g. Assign outputs from intermediatesignals
-------------------------------------------
buff_o <= buff;

## Slide 25: Testbench for Lab3 – Exercise 1.1) [Page 1/2]
-- Testbench-Code: testbench_rsff.vhd
-- History: ...
-- Library & Use Statements
LIBRARY ieee;
USE ieee.std_logic_1164.all;
-- Entity Declaration
ENTITY testbench_einfach_schaltung IS
END testbench_einfach_schaltung;
-- Architecture Declaration
ARCHITECTURE struct OF testbench_einfach_schaltung IS
-- Component Declaration
COMPONENT einfach_schaltung
PORT ( clock : in std_logic;
reset_n : in std_logic;
data_i : in std_logic;
hold_i : in std_logic;
buff_o : out std_logic );
END COMPONENT einfach_schaltung;
-- Signals & Constants Declaration
SIGNAL t_clock : std_logic;
SIGNAL t_reset_n : std_logic;
SIGNAL t_data_i : std_logic;
SIGNAL t_hold_i : std_logic;
SIGNAL t_buff_o : std_logic;
CONSTANT clk_halfp : time := 0.5 us;
-- Begin Architecture
BEGIN
-- Instantiation DUT (Device under Test)
dut: einfach_schaltung
PORT MAP( clock => t_clock,
reset_n => t_reset_n,
data_i => t_data_i,
hold_i => t_hold_i,
buff_o => t_buff_o );
-- Clock Generation Process (with wait)
clock_gen: PROCESS
BEGIN
t_clock <= '0';
WAIT FOR clk_halfp;
t_clock <= '1';
WAIT FOR clk_halfp;
END PROCESS clock_gen;

## Slide 26: Testbench for Lab3 – Exercise 1.1) [Page 2/2]
-- Stimuli and Check Process (wait & ASSERT) stimuli: PROCESS
BEGIN
-- initialize all inputs and activate reset_n to initialize the DUT
t_reset_n <= ‘0'; t_data_i <= '1'; t_hold_i <= '0';
WAIT FOR 10*clk_halfp;
-- release reset_n and wait 2 clock-periods
WAIT UNTIL t_clock = '0';
t_reset_n <= '1';
WAIT FOR 2*clk_halfp;
-- since hold was not active, after clock rising edge check that buff_o = data_i
WAIT UNTIL t_clock = '0';
ASSERT (t_buff_o = t_data_i) REPORT "TEST_1: buff_o not equal data_i" SEVERITY ERROR ;
WAIT FOR 2*clk_halfp; ...
-- change data_i and check that buff_o follows
WAIT UNTIL t_clock = '0';
t_data_i <= '0';
WAIT FOR 2*clk_halfp;
Assert (t_buff_o = t_data_i) REPORT "TEST_2: buff_o not equal data_i" SEVERITY ERROR ;
-- now set hold and check that buff_o do not -- follow data_i changes
WAIT UNTIL t_clock = '0';
t_hold_i <= '1'; t_data_i <= '1';
WAIT FOR 2*clk_halfp;
ASSERT (t_buff_o /= t_data_i) REPORT "TEST_3: buff_o equal data_i" SEVERITY ERROR ;
-- stop simulation
WAIT FOR 10*clk_halfp;
ASSERT (FALSE) REPORT "Test programm beendet" SEVERITY FAILURE;
END PROCESS stimuli;
-- End Architecture
END struct;

## Slide 27: VHDL Simulator
Entity: A
Architecture: A
Entity: B
Architecture: B
Package: A
VHDL Simulator
Working Library
ieee Library
.
.
Primitive Libraries
.
.

## Slide 28: edaverzeichnis
simulation
source
synthese
modelsim
scripts
Projekt
.vhdl
.do
work

## Slide 29: Compile Script (compile.do) for VHDL Simulation
# create work library
vlib work
# compile project files
vcom -2008 -explicit -work work ../../source/testbench_einfach.vhd
vcom -2008 -explicit -work work ../../source/einfach.vhd
# run the simulation
vsim -novopt -t 1ns -lib work work. testbench_einfach
do ../scripts/wave.do
run 1800.0 ns
starts simulator
create work directory „work“ to store ModeSim compiled data
compiles VHDL source files and store compiled data in „work“ dir
run simulation for 1800 ns
open Waveform Window with saved preferences

## Slide 30: Simulator ModelSim: Getting Started
Creating a new Project
Select project directory
where «work» compiled director will
Be generated
Start simulation with script in the command line

## Slide 31: Waveform Window
Objects Window (to select Signals for visualisation)
Structure Window (Design Hierarchy Browser)
Add Wave

## Slide 32: Library Window

## Slide 33: VHDL Templates
Block Design (RTL)
Block Design (Hierarchical)
Testbench (Hierarchical & Behavioural)

## Slide 34: Template _ Block Design (RTL)
-- Library & Use Statements
-- Entity Declaration
-- Architecture Declaration -- Signals & Constants Declaration
-- Begin Architecture
-------------------------------------------
-- Process for combinatorial logic
------------------------------------------- -- Process for registers (flip-flops)
-------------------------------------------
-- Concurrent Assignements
-- e.g. Assign outputs from intermediate signals -------------------------------------------
-- End Architecture

## Slide 35: Template _ Block Design (Hierarchical)
-- Library & Use Statements
-- Entity Declaration
-- Architecture Declaration -- Components Declaration
-- Signals & Constants Declaration
-- Begin Architecture
-------------------------------------------
-- Instantiation Block - 1
------------------------------------------- -- Instantiation Block – 2 ...
-------------------------------------------
-- Concurrent Assignments
-- e.g. Assign outputs from intermediate signals -------------------------------------------
-- End Architecture

## Slide 36: Template _ Testbench (Hierarchical & Behavioural)
-- Library & Use Statements
-- Entity Declaration
-- Architecture Declaration -- Component Declaration
-- Signals & Constants Declaration
-- Begin Architecture
-------------------------------------------
-- Instantiation DUT (Device under Test)
------------------------------------------- -- Clock Generation Process (with wait)
-------------------------------------------
-- Stimuli and Check Process (with wait & ASSERT) -------------------------------------------
-- End Architecture
non
synthetisisable
commands